## Slide 1: 2016 Customers Meeting

## Slide 2: PRODUCTS OVERVIEW
Pressure switches for water pumps
Electronic controllers for water pumps
Variable frequency drivers for water pumps

## Slide 3: PRESSURE SWITCHES FOR WATER PUMPS
PM-PT
PM/5-3W PT/5-3W
LP/3
MODEL | RANGE | RATINGS
PM/5 | 1-5 bar | 250V 16(10A)
PM/6 | 1,5-5,5 bar | 250V 16(10A)
PM/12 | 3-12 bar | 250V 16(10A)
PT/5 | 1-5 bar | 500V 16(10A)
PT/6 | 1,5-5,5 bar | 500V 16(10A)
PT/12 | 3-12 bar | 500V 16(10A)
MODEL | RANGE | RATINGS
PM/5-3W | 1-5 bar | 250V 16(10A)
PT5-3W | 1-5 bar | 500V 16(10A)
MODEL | RANGE | RATINGS
LP/3 | 0,05-0,4 bar | 250V 16(10A)
LP/3-18 | 0,5-2,0 bar | 250V 16(10A)

## Slide 4: APPLICATIONS
PM/5-3W

## Slide 5: ADVANTAGES
DIFFERENT SETTINGS AVAILABLE
CAN BE USED IN VARIOUS SYSTEMS WITH DIFFERENT PUMPS
GRADUATED SCALE
EASY SETTING OF PRESSURE
FULLY INSULATED TERMINALS
IMPROVED SAFETY
REVOLVING NUT
QUICK CONNECTION
TEAR-RESISTANT CABLE CLAMPS
IMPROVED SAFETY

## Slide 6: ELECTRONIC CONTROLLERS FOR WATER PUMPS
BRIO 2000-M
BRIO TANK
BRIO TOP
Pressure and flow controller | 
Supply | 230V 50-60Hz 12A max.
Pressure and flow controller with embedded pressure tank | 
Supply | 230V 50-60Hz 12A max.
Pressure and flow controller with display and advanced features | 
Supply | 230V 50-60Hz 16A max.

## Slide 7: APPLICATIONS
IRRIGATION
DOMESTIC WATER SYSTEMS
INDUSTRIAL
RESIDENTIAL

## Slide 8: ADVANTAGES
ADJUSTABLE CUT-IN PRESSURE
ONE UNIQUE MODEL CAN BE USED UP TO 35m HEIGHT
RATED IP65
CAN BE INSTALLED OUTDOOR WITHOUT ADDITIONAL PROTECTION
COMPACT DESIGN
CAN BE INSTALLED EVERYWHERE
IN VERTICAL OR HORIZONTAL POSITION
INTEGRATED PRESSURE GAUGE
NO NEED OF EXTERNAL ACCESSORIES
VERY LOW PRESSURE DROP
DOESN’T AFFECT PUMP PERFORMANCE
MAXIMUM LOAD 12A
CAN BE USED WITH PUMPS UP TO 2HP
AUTOMATIC RESET
PUMP RESTART AUTOMATICALLY AFTER DRY RUNNING

## Slide 9: BRIO TANK
0,4LT INTEGRATED PRESSURE TANK WITH EPDM BLADDER
REDUCES HAMMERING
REDUCES RESTARTS OF THE PUMP
HELPS TO STABILIZE PRESSURE IN THE SYSTEM WHEN THE PUMP STOPS
LOW STAND-BY POWER
ELECTRONIC BOARD IS COLD AND AVOID CONDENSATION
INSPECTIONABLE VALVE
VALVE CAN BE CLEANED FROM IRON AND SAND
PRE-CHARGE PRESSURE VALVE
PRE-CHARGE PRESSURE CAN BE INSPECTED AND CHANGED
OPTIONAL PRESSURE GAUGE HELPS TO VERIFY INTERNAL PRESSURE.

## Slide 10: BRIO TOP
5 LANGUAGES LCD
EASY SETTING OF PARAMETERS
DIGITAL INDICATION OF PRESSURE AND CURRENT
CURRENT CONTROL
PROTECTS THE PUMP AGAINST OVERLOAD
RATED 16A
CAN BE USED WITH PUMPS UP TO 3HP
I/O CONNECTIONS
CAN BE CONNECTED TO BMS AND OTHER EQUIPMENTS FOR REMOTE CONTROL
ALLOWS CONNECTION OF 2 DEVICES IN BOOSTER SETS
ERROR LOG
ERROR LOGGING FOR AN EASIER AND COMPLETE TROUBLESHOOTING

## Slide 11: WHY TO CHOOSE BRIO TOP ?
P+F MODE
PUMP STARTS ON PRESSURE DROP AND STOPS ON ZERO FLOW
NO NEED OF PRESSURE TANK
MAXIMUM PRESSURE CANNOT BE ADJUSTED
P+P MODE
PUMP STARTS AND STOPS ACCORDING TO PRESSURE THRESHOLD
MUST BE USED WITH A PRESSURE TANK, LIKE A PRESSURE SWITCH
CUT-IN AND CUT-OFF PRESSURE CAN BE REGULATED
2 PRODUCTS IN ONE!
Mode
P + F
Mode
P + P

## Slide 12: WHY TO CHOOSE BRIO TOP ?
BOOSTER SETS WITHOUT CONTROL BOX!
P+P MODE
WHEN USED IN P+P MODE WITH A PRESSURE TANK, 2 DEVICES CAN BE INTERCONNECTED TO GET A BOOSTER SET
PUMPS START IN SWAPPED MODE ON WATER DEMAND
PUMPS CAN RUN TOGETHER IN CASE OF HIGH WATER REQUEST FROM THE USERS
JUST A 4 WIRE CABLE IS NEEDED FOR INTERCONNECTION

## Slide 13: WHY TO CHOOSE BRIO TOP ?
CAN BE CONNECTED TO OTHER DEVICES
AUXILIARY I/O
INPUT CAN BE USED TO CONNECT A FLOAT SWITCH OR A TIMER
CAN BE REMOTELY OPERATED FROM ANOTHER DEVICE (PLC, COMPUTER WITH “CAFM”, ETC.)
OUTPUT RELAY CAN SIGNAL ERROR CONDITIONS OR CAN BE USED TO START OTHER EQUIPMENT (UV UNITS, CHLORINE PUMPS, ETC.)
CAN BE USED TO INTERFACE THE PUMP TO BMS (BUILDING MANAGEMENT SYSTEMS)

## Slide 14: WHY TO CHOOSE BRIO TOP ??
ADVANCED PROTECTIONS AND FEATURES
OVER CURRENT
Stops the pump when the current overcomes the maximum programmed value (locked rotor)
OVER PRESSURE
Stops the pump when the pressure overcomes the maximum programmed value (useful for applications with variable suction depth)
ICE PROTECTION
If temperature falls below 4°C, pump starts automatically for 15” every 15 minutes to prevent freezing of water inside the impellers
ANTI-SEIZE FUNCTION
When the pump is not used for a period longer than 24H, Brio Top will start the motor automatically to prevent rotor seizure

## Slide 15: INVERTERS FOR WATER PUMPS
SIRIO
SIRIO ENTRY – SIRIO ENTRY XP
NETTUNO
1-PH 230V INPUT / 3-PH 230V OUTPUT
For 3-phase pumps, delta connection, Output max. 9,7A
Water cooling – pipe mounting
1-PH 230V INPUT / 1-PH 230V OUTPUT
For 1-phase pumps with capacitor, Output max. 10,5A Sirio Entry Output max. 14A Sirio Entry XP
Water cooling – pipe mounting
3-PH 400V INPUT / 3-PH 400V OUTPUT
For 3-phase pumps, star connection, Output max. 13A Output max. 9A Output max. 6A
Air cooling – wall mounting

## Slide 16: ADVANTAGES
COMPACT DESIGN
CAN BE INSTALLED EVERYWHERE
IN VERTICAL OR HORIZONTAL POSITION
8 LANGUAGES LCD
EASY SETTING OF PARAMETERS
DIGITAL INDICATION OF PRESSURE AND CURRENT
ERROR LOG
INTEGRATED PRESSURE SENSOR
NO NEED OF EXTERNAL SENSOR
NO EXTRA COSTS
WATER COOLING
LONG LIFE OF POWER ELECTRONIC CIRCUITS,
HIGH POWER RATINGS IN A SMALL DESIGN
VARIABLE SPEED
CONSTANT PRESSURE AND ENERGY SAVING

## Slide 17: WHAT IS NEW ON SIRIO 2.0?
User friendly new interface:
3.0 BAR
40 Hz
Vin= 230V
I= 6.0A
Tm=45°C
Ta=45°C
Language
EN
All functioning variables available on the LCD (pressure, voltage, temperature)
End user can only change the language (to prevent unauthorized variation of parameters)

## Slide 18: WHAT IS NEW ON SIRIO 2.0?
Improved I/O:
Aux. Con.
1 <->
I/O input
‘2’ 
I/O output
ERR.
Optional I/O card:
1 digital input for external start, external error or double set-point
1 digital output for “error” signaling, “pump in function” signaling or for auxiliary fixed speed pump
Standard Aux. Connector: allows the connection of 2 Sirio in a booster set; otherwise can be used for external start or double set-point command

## Slide 19: WHAT IS NEW ON SIRIO 2.0?
Intelligent thermal management:
T.a. max
80°C
automatically reduces the power to the pump when the temperature increases
avoids over-temperature on the IGBT and DC bus capacitors
extends inverter life

## Slide 20: WHAT IS NEW ON SIRIO 2.0?
Improved pressure sensor amplification circuit:
Pr. Calibr.
0.0 BAR
improved pressure reading
reduced drift of the signal along the time
increased amplification gain for a more accurate pressure reading
Pr. Calibr.
5.0 BAR

## Slide 21: WHAT IS NEW ON SIRIO 2.0?
Complete error log:
E0 (000)
Low Voltage
Complete error log
13 different error codes with full text explanation
Value between brackets indicates number of occurrences for one error
Timer of “power supply time” and “pump running time”
E1 (000)
High voltage
E13 (000)
Press.Sens.
E6 (000)
Dry Running

## Slide 22: WHAT IS NEW ON SIRIO 2.0?
Can operate with impure water:
Flow sensor can be disabled
The drive can be operated according only to the pressure
Useful for application with sand and iron
Dry running pressure must be set to correctly stop the pump in absence of water
Flow sens.
OFF
Dry ru. Press.
0,5 BAR

## Slide 23: WHAT IS NEW ON SIRIO 2.0?
New board to board connection:
Boards are internally connected through ribbon flat cable instead of pin strips
Increased reliability
No loose of signal
Easier replacement of the boards during service

## Slide 24: WHAT IS NEW ON SIRIO 2.0?
New configuration possibilities:
DeltaP stop: when the actual pressure overcomes the value of “set-point+deltaP stop” the drive will stop the pump immediately, without delay.
DeltaP Stop
2.0 BAR
Full reset
ON
Additionally to the dry running automatic reset, a full reset function can be enabled to automatically restart the pump after any error (under voltage, over voltage, over temperature, etc.)

## Slide 25: WHAT IS NEW ON SIRIO 2.0?
Rated frequency: the maximum rated frequency of the pump can be selected between 50 and 60 Hz
Nom.Freq.
50 Hz
Freq. Corr.
+5 Hz
Frequency correction: allows to apply a correction to the rated frequency from -5 up to +5 Hz. Can be used to limit or to extend the power of the pump.

## Slide 26: WHAT IS NEW ON SIRIO 2.0?
Functioning mode can be changed between AUTOMATIC (pressure) or MANUAL.
Manual mode allows to test the pump at different frequencies, without the closed-loop pressure control.
Command
MAN
2.0 BAR
55 Hz

## Slide 27: WHAT IS NEW ON SIRIO 2.0?
More than 20 improvements were applied to the circuit boards:

## Slide 28: WHAT IS COMING ON??
 | INPUT | OUTPUT
NETTUNO 3P 13A | 3X400V | 3X400V – 13A max.
NETTUNO 3P 9A | 3X400V | 3X400V – 9A max.
NETTUNO 3P 6A | 3X400V | 3X400V – 6A max.
Nettuno
 | INPUT | OUTPUT
NETTUNO UNIVERSAL | 1X230V | 1X230V – 10,5A max. 3X230V – 9,7A max. (selectable)
Nettuno Universal

## Slide 29: NETTUNO
Wall mounting
Pipe mounting

## Slide 30: NETTUNO
ANALOG INPUTS
4-20mA (TRANSDUCER)
0-10V (AUXILIARY)
RS 485
UP TO 8 PUMPS CONNECTED ON BOOSTER SET
DIGITAL OUTPUTS
2X OUTPUTS (ERROR, PUMP ON, DOL PUMP)
DIGITAL INPUTS
1X ENABLE
1X ERROR
1X SECONDARY SET-POINT
POWER OUTPUT
400V – 3 MODELS AVAILABLE FOR 6, 9 AND 13 A MAX. LOAD
POWER INPUT
400V – 50/60Hz
DISPLAY
LCD 16X2 – EASY CONFIGURATION

## Slide 31: THANKS FOR YOUR ATTENTION!